## Slide 1: CompTIA IT Fundamentals Study Guide (FC0-U61)
Chapter 1:
Core Hardware Components

## Slide 2: Chapter 1: Core Hardware Components
Illustrate the basics of computing and processing
  Input
  Processing
  Output
  Storage
Compare and contrast common units of measure
  Storage unit
    Bit
    Byte
    KB
    MB
    GB
    TB
    PB
  Processing speed
    MHz
    GHz
Explain the purpose of common internal computing components
  Motherboard/system board
  Firmware/BIOS
  RAM
  CPU
    ARM
      Mobile phone
      Tablet
    32-bit
      Laptop
      Workstation
      Server
    64-bit
      Laptop
      Workstation
      Server
  GPU
  Storage
    Hard drive
    SSD
  Cooling
  NIC
    Wired vs. wireless
    Onboard vs. add-on card

## Slide 3: Chapter 1: Core Hardware Components (con’t.)
Compare and contrast storage types
  Volatile vs. non-volatile
  Local storage types
    RAM
    Hard drive
      Solid state vs. spinning disk
    Optical
    Flash drive

## Slide 4: Introducing Internal Components
Replaceable components are called field replaceable units (FRUs)
The case protects internal components

## Slide 5: Motherboard Overview
Connect all components together
Also called system board or mainboard
Form factor refers to size and shape
Chipset is the technology on the motherboard – perform interface and peripheral functions

## Slide 6: Motherboard Connectivity
Contains sockets or slots for:
  Processor (CPU)
  Memory (RAM)
  Expansion cards (PCI, PCIe)
  Disk controllers (PATA, SATA)
  Power connectors
  BIOS/firmware
  CMOS and CMOS battery
  Back panel connectors
  Front panel connectors

## Slide 7: Processors (CPUs)
Central Processing Unit (CPU)
  The “brain” of the computer
Intel and AMD major manufacturers
Speed measured in gigahertz (GHz)
Processors perform binary math

## Slide 8: Processors (CPUs)
CPU slots usually square
  Pin Grid Array (PGA), Land Grid Array (LGA)
Characteristics
  Architecture
    32-bit
    64-bit
    ARM
  Speed
    GHz – billion cycles per second
  Cache
    Built-in memory, small and fast

## Slide 9: Memory
Read only memory (ROM)
  Permanent, no changes allowed
  Example: BIOS
Random access memory (RAM)
  Can be static or dynamic
    Static is nonvolatile, like a thumb drive
  Dynamic used inside computers
    Analogous to short-term memory
    Needs power to retain contents

## Slide 10: More Memory
Form factors:
  Desktops
    Double data rate 2 (DDR2)
    Double data rate 3 (DDR3)
    Double data rate 4 (DDR4)
  Laptops
    Small outline dual inline memory module (SODIMM)
Virtual Memory

## Slide 11: Hard Drives
Permanent long-term storage
Size usually in hundreds of gigabytes (GB) or terabytes (TB)
Spinning (or mechanical) hard disk drives (HDD) versus solid state hard drives (SSD)
Connected via SATA or PATA

## Slide 12: Optical drives
CD-ROM
  Compact Disc Read Only Memory
DVD-ROM
  Digital Video Disc Read Only Memory
BD-ROM
  Blu-ray Read Only Memory

## Slide 13: Power, BIOS, and CMOS Battery
Power Connectors for power supply
Basic Input/Output System (BIOS) boots the system and initiates hard drive and memory
Complimentary Metal Oxide Semiconductor (CMOS) chip holds BIOS
  CMOS battery helps chip store BIOS information when powered off

## Slide 14: Back and Front Panel
Back panel connectors
  For keyboards, mice, network cables, and more
  Will cover in detail in Chapter 2
Front panel connectors
  Power and reset buttons
  Drive activity lights
  Audio ports
  Other connectors, such as USB

## Slide 15: Video Cards
Also called graphics cards or video adapters
Responsible for rendering video
  Monitor is connected to them
Good ones will have a graphics processing unit (GPU) and their own memory
Typically PCIe

## Slide 16: Sound Cards
Produce sound
Often integrated into the motherboard

## Slide 17: Network Cards
Network Interface Card (NIC)
Allow the computer to participate on a network
Wired (needs a cable to send/receive network signals) or wireless (no cable needed)

## Slide 18: Modems
Practically obsolete today
Allows a computer to participate on a network via standard telephone lines

## Slide 19: Power Supplies
Power Supply Unit (PSU)
Converts AC from wall to DC the computer needs
Capacity measured in watts
Has connectors for the motherboard as well as peripherals such as hard drives, optical drives, and video cards

## Slide 20: Cooling Systems
Computers get hot – components such as the processor can melt
Case cooling
  Front intake fan
  Rear exhaust fan
  Power supply exhaust fan
CPU cooling
  On the processor itself
  Usually heat sink and a fan
  Liquid cooling and other advanced methods available