## Slide 1: CompTIA Network+ Certification
2.3 IPv6 Addressing

## Slide 2
Describe hex notation and IPv6 address compression and packet structure
Configure an appropriate IPv6 addressing scheme
Configure an IPv6/IPv4 tunneling mechanism
Notes: The number in the bottom right corner of the slides refers back to the page where this topic starts in the course book.

## Slide 3: IPv6 Address Format
IPv4 address shortage
  32-bit address space
  Inefficiently allocated
  Complex routing tables
IPv6/IPng
  128-bit address space
  Cope with mobile/“Internet of Things” growth
  Hierarchical address allocation (simpler routing)
Very slow transition!

## Slide 4: Hexadecimal Numbering
Base 10 (decimal) - 0-9 and place value powers of 10
Base 2 (binary) - 0 or 1 and place value powers of 2
Base 16 (hex) - up to 16 values represented by 0-9 and A, B, C, D, E, F
  1 hex digit can represent 4 binary digits (a “nibble”)
  2 hex digits can represent 1 octet (byte/8 bits)
  4 hex digits can represent 1 double-byte (16 bits)
  Can be identified by leading 0x – e.g “0xFF” – or trailing h – e.g “FFh”

## Slide 5: IPv6 Address Compression
128-bit binary address = lots of typing!
    0010 0000 0000 0001 : 0000 1101 1011 1000 : 0000 0000 0000 0000 : 0000 0000 0000 0000 : 0000 1010 1011 1100 : 0000 0000 0000 0000 : 1101 1110 1111 0000 : 0001 0010 0011 0100
Hex notation
  Each hex digit represents 4 binary digits
  Hex digits are arranged in 8 x 16-bit (double byte) blocks separated by colons
    2001:0db8:0000:0000:0abc:0000:def0:1234
Zero compression
  Can omit leading zeroes
  Can compress one sequence of “all zero” double bytes
    2001:db8::abc:0:def0:1234

## Slide 6: IPv6 Packets

## Slide 7: IPv6 Addressing Schemes
In IPv6, host bits are fixed
  Network ID (64-bit)
  Host ID (64-bit)
  Network prefix (e.g. /48 or /64) determines whether hosts are on same network
Addressing schemes are different to IPv4
  Unicast
  Multicast
    Must be supported
    No broadcasts
  Anycast

## Slide 8: IPv6 Unicast Addressing (1)
Globally scoped
  001 binary prefix (2 or 3 in hex)
  Next 45 bits allocated to registries and ISPs
  Following 16 bits for subnetting
  64 bits for interface ID
Interface ID/EUI-64
  MAC-derived/EUI-64
  Pseudo-random token

## Slide 9: IPv6 Unicast Addressing (2)
Link-local scope
  1111111010 binary prefix (or fe80 in hex)
  Not routable
  Communicate with same subnet (neighbors)
  All interfaces have link-local addresses
Unique Local Addressing
  Addresses routable only within a site
  Can never route over the Internet
  fd00::/8 prefix with 40-bit pseudo-random site ID

## Slide 10: IPv6 Multicast and Anycast
Multicast Addressing
  Multicast support not optional like IPv4
  8-bit multicast scope (11111111 or ff in hex)
  4-bit flag
  4-bit scope (link-local/global)
  112-bit group ID
  Link-local multicast replaces broadcast
Anycast
Unspecified (::) and loopback (::1)

## Slide 11: IPv6 Address Prefixes

## Slide 12: IPv6 Address Autoconfiguration
Stateless Address Autoconfiguration (SLAAC)
  Generate a unique link-local address
  Listen for Router Advertisements
Neighbor Discovery Protocol
  Replaces ARP
  Address autoconfiguration
  Prefix discovery
  Local address resolution
  Redirection
Multicast Listener Discovery Protocol
  Allows nodes to join a multicast group
  Discover whether group members are present on the local subnet

## Slide 13: ICMPv6
Updates Internet Control Messaging Protocol for IPv6
Error messaging
  Destination unreachable, time exceeded, and so on as per ICMPv4
  Packet to big (hosts must perform fragmentation)
Informational messaging
  Echo and redirect as per ICMPv4
  Messages to support SLAAC, ND, and MLD
  Router/neighbor advertisements and solicitations

## Slide 14: Migrating to IPv6
Dual-stack IPv4 and IPv6 routing
  ISATAP (Intra-Site Automatic Tunnel Addressing Protocol)
  IPv4 mapped addresses
IPv6 tunneling
  6to4 – encapsulate IPv6 packets in IPv4 packets
  Implemented by Teredo (Windows) and Miredo (Linux)
  4to6 – tunnel IPv4 over IPv6 but not widely required!

## Slide 15
IPv6 uses 128-bit addresses with variable length network prefixes and a 64-bit host ID derived from the MAC address or randomly assigned.
IPv6 supports global and link-local address schemes and unicast, multicast, and anycast addressing.
In IPv6, SLAAC, ND, MLD, ICMPv6, and DHCPv6 are used for autoconfiguration and neighbor discovery.
Communication can take place between IPv4 and IPv6 using dual stack hosts or tunneling.
Notes:   Convert the binary value "1010 0001 1000 1100" to hex. A18C.
  Which of the following IPv6 addresses is a valid unicast host address?
        fe80::218:8bff:fea7:bd37 – TRUE
        fe80::219:d2ff::7850 – FALSE
        ff02::219:d2ff:fea7:7850 – FALSE
        ::/128 - FALSE
  What is an EUI-64 and how might it be used by IPv6? Extended Unique Identifier (EUI) is IEEE's preferred term for a MAC address. EUI-64 is a 64-bit hardware interface ID. A 48-bit MAC address can be converted to an EUI-64 using a simple mechanism. The EUI-64 can be used as the IPv6 interface ID, though a randomly generated token is often preferred.
  In IPv6, how is the loopback address best expressed? ::1.
  In IPv6, how could you distinguish a unicast address with global scope from other addresses? Starts with binary "001" or hex "2" or "3".
  If assigned a single global IPv6 address prefix, how many bits are available for subnetting? 16 bits.
  What type of IPv6 unicast address is not routable? Link-local address (and Unique Local Addresses (ULA).
  What is anycast? A special type of multicast where a message can be sent to any member of a group (the closest available one) but not all of them.
  In IPv6, how can a client obtain a routable IPv6 address without requiring manual configuration? Stateless Address Autoconfiguration (SLAAC) allows a host to autoconfigure an interface by listening for Router Advertisements to obtain a network prefix.
  What is 6to4? A method of tunneling IPv6 packets over a IPv4 network.

## Slide 16
Lab 5 / Configuring IPv6 Networking
Notes: Note that there are three sets of labs available to use with this course:
        Classroom labs that you set up and run yourself (refer to the separate "Labs" book and setup guide on the instructor resource support site).
        Learn On Demand (LOD) hosted classroom labs accessed via a browser but following the same general sequence and steps as the classroom lab book.
        Self-study Online Labs from Practice Labs accessed by students online - these labs are intended for use by students studying independently and are different from the classroom and hosted classroom labs. If you are using Practice Labs online labs in the classroom, you must specify this at the time of purchase so that the appropriate bandwidth is provisioned in advance. Please ensure that the student PCs meet the requirements for accessing the Self-study Online Labs series. You can obtain a setup guide at gtsgo.to/nf1rc
The sequence of classroom and hosted classroom labs is shown on this slide and in the margins of your instructor edition and in the course timetable. You should guide the students to complete each lab.
If you are not using the classroom or LOD hosted classroom labs you should delete this slide.